Analytical and Technical Features

| ECS 8020 features |
| --- |
| Type | CHNS-O |  |
| Analysis time | CN | 5 min |
|  | CHN | 8 min |
|  | CHNS | 13/25 min |
|  | O | 4 min |
| Analytical range | C | 0.002-20 mg |
|  | H | 0.002-5 mg |
|  | N | 0.002-2 mg |
|  | S | 0.002-6 mg |
|  | O | 0.002-2 mg |
| Accuracy | <0,3% |  |
| Precision | <0,3% |  |
| Sampler | Pneumatic autosampler | 147 positions |
|  | Electronic autosampler | 32, 50 100 positions |
|  | Manual | - |
| Dual furnace system |  |  |
| Touch screen display |  |  |
| Stand-by mode |  |  |

:

| Physical specifications |
| --- |
| Dimensions | 81x50x37cm |
| Weight | 68kg |
| Power supply | 230V, 50/60Hz |
| Power absorption | 5A, 1100Wh |
| Gas requirements | Helium (99.999% purity), 3-5 bar |
|  | Oxygen (99.999% purity), 3-5 bar |
|  | Air (oil free compressed air) |

| Analytical conditions |
| --- |
| Gas carrier | Helium |
| Leak test | Automatic leak test |
| Furnace temperature | Left furnace max 1100°C |
|  | Right furnace max 1100°C |
| Oven temperature | Max 110°C |
| Oxygen volume need | Automatically calculated by the oxygen doser |
| Fluxes regulation | Electronic fluxes regulation |
| Gas separation | 0.8-4 m GC column |
| Detector | High Sensitivity TCD |
| Software data analysis | EAS Clarity |
| Calibrations | Linear, Quadratic, cubic |
| Active calibration | As necessary |

| Sample |
| --- |
| Sample size | 0,1-500 mg (depending on sample nature) |
|  | up to 1000mg for soil samples |
|  | Up to 100mg for coal |
| Sample type | Liquid |
|  | Solid |
| Capsule | High purity tin and silver capsules |

| Accessories |
| --- |
| Kit |  |
| Balance |  |
| Consumables | Proprietary NC Technologies S.r.l. |
| Assistance by phone or email within 24 hours |

| Approvals |
| --- |
| AOAC Official Method 993.13 | ISO 15178:200 | ISO 29541:2010 |
| ISO 10694, 1995 | ASTM Method D 5291-09 | ISO 16948, 2015 |
| ISO 13878, 1998 | ASTM Method D 5373-02 | EN 15407:2011 |
| UNI EN 13654-2:2001 | ASTM Method D 5622 | ASTM Method D 1552 |
| EPA Method 440.0, 1997 | ASTM Method D 7633-13 | ISO D 3176-09 |
| EN 13137 (2001-12) |  |  |